## Slide 1: 2018 Moving Rainbow LED Kit
Arduino Moving Rainbow
Arduino Nano (CH340 driver)
1/2 breadboard (400 tie points)
USB cable (mini-b)
30 pixel NeoPixel strip with GND (black), 5v (red) and data (yellow)
Momentary push buttons and wire
Kit Contents
Download the Arduino IDE software from https://www.arduino.cc/en/Main/Software
Step 1: Download the Arduino Integrated Development Environment (IDE)
Step 2: Install the NeoPixel Library
Download CH341 driver from: http://www.wch.cn/download/CH341SER_ZIP.html (Chinese)
Step 3: Install the CH340 Driver
Step 5: Run the NeoPixel Example Strandtest
Step 6: Open the Moving Rainbow Labs
Open: http://moving-rainbow.readthedocs.io/en/latest/README/
Step 4: Set the Board to Nano and Port to /dev/cu.wchusbserial1420
Note on Windows the port name is “COM3”
or “COM4”

## Slide 2: NeoPixel Code Examples
#include <Adafruit_NeoPixel.h>
#define LEDPIN 12 // connect the Data from the strip to this pin on the Arduino
#define NUMBER_PIXELS 30 // the number of pixels in your LED strip
Adafruit_NeoPixel strip = Adafruit_NeoPixel(NUMBER_PIXELS, LEDPIN, NEO_GRB + NEO_KHZ800);
Sample Preamble
void setup() {
strip.begin(); // initialize all the variables – don’t forget this line!
strip.setPixelColor(0, 255, 125, 0); // set pixel 0 to be yellow
strip.show(); // send the data to the LED strip – must do this after any change
delay(1000); // wait 1 second
}
Sample Setup
void loop() {
for (int i=0; i<NUMBER_PIXELS; i++) {
strip.setPixelColor(i, 255, 0, 0); // turn the "i"th pixel on
strip.show(); // send the data to the LED strip
delay(100); // wait 1/10th of a second – a lower number makes it go faster
strip.setPixelColor(i, 0, 0, 0); // turn the "i"th pixel off
strip.show(); // send the data to the LED strip
delay(100); // wait 1/10th of a second – a lower number makes it go faster
}
}
Sample Moving Pixel
Get the first pixel to flash red on for 1 second and off for 1 second
Change the speed of flashing to be 1/10th of a second on and 1/10th of a second off
How fast can you make the first pixel flash?
Can you change the color of the first pixel (red, green, blue)
Run NeoPixel example programs (strandtest)
Find Moving Rainbow examples
Work though various examples
On moving rainbow github/src find mini-maker-fair LED strip two buttons program
Wire button from D2 and D3 (interrupts) to ground through a momentary push button
Try all the modes
Create your own mode pattern
Can you create a game? Can you trap a moving pixel in a “jail” to get a point?
Sample Labs