## Slide 1: 2017 HackDay LED Kit
Arduino Nano (CH340)
1/2 breadboard (400 tie points)
330 Ohm Resistor
LED – max current 20ma
USB cable (mini-b)
30 pixel NeoPixel strip with GND (black), 5v (red) and data (yel.)
Momentary push buttons and wire
3 AAA battery pack with switch
3 AAA batteries
Arduino Moving Rainbow
Kit Contents
Learn how to solder solid wires to ends of battery pack
Hook up battery to breadboard rails
Hook up LED circuit in series with 330 ohm resistor
Add a button to turn on and off the LED
Plug in Arduino Nano to breadboard
Connect 5v and GND wires and verify LEDs on Arduino work
Download Arduino IDE software and plug in USB cable
Get "blink" lab to work (configure board and port) and use upload button
Download NeoPixel libraries
Connect NeoPixel strip to pin 12
Run NeoPixel example programs (strandtest)
Find Moving Rainbow examples
Work though various examples
On moving rainbow github/src find mini-maker-fair LED strip two buttons program
Wire button from D2 (interrupt) to ground
Try all the modes
Create your own mode
Sample Labs

## Slide 2: NeoPixel Code Examples
#include <Adafruit_NeoPixel.h>
#define LEDPIN 12 // connect the Data from the strip to this pin on the Arduino
#define NUMBER_PIXELS 30 // the number of pixels in your LED strip
Adafruit_NeoPixel strip = Adafruit_NeoPixel(NUMBER_PIXELS, LEDPIN, NEO_GRB + NEO_KHZ800);
void setup() {
strip.begin(); // initialize all the variables – don’t forget this line!
strip.setPixelColor(0, 255, 125, 0); // set pixel 0 to be yellow
strip.show(); // send the data to the LED strip – must do this after any change
delay(1000); // wait 1 second
}
Download the Arduino IDE software from https://www.arduino.cc/en/Main/Software
void loop() {
for (int i=0; i<NUMBER_PIXELS; i++) {
strip.setPixelColor(i, 255, 0, 0); // turn the "i"th pixel on
strip.show(); // send the data to the LED strip
delay(100); // wait 1/10th of a second – a lower number makes it go faster
strip.setPixelColor(i, 0, 0, 0); // turn the "i"th pixel off
}
}
Step 1: Download the IDE
Step 2: Install the NeoPixel Library
Step 3: Install the CH340 Driver
Download CH341 driver from: http://www.wch.cn/download/CH341SER_ZIP.html
Step 4: Open the Moving Rainbow Labs
Open: http://moving-rainbow.readthedocs.io/en/latest/README/
Sample Preamble
Sample Setup
Sample Moving Pixel